## Slide 1
CAVA TRAINING SERIES
Using the
CAVA Platform
MODULE 2
29 September 2026
10:00–11:30 · Online
From a project question to a usable climate signal
Notes: Screenshot updated for the current CAVA Platform interface on 28 September 2026. Source: https://cavaplatform.fao.org/map

## Slide 2
Today’s route
A guided demonstration, with time to interpret and try the controls
CAVA MODULE 2
02
05
min
Start with a project question
Choose the information we need
45
min
Explore the Platform
Select an indicator, then compare periods and scenarios
15
min
Read the climate signal
Look at magnitude, pattern and uncertainty
10
min
Try it yourself
Repeat the workflow for your own area
10
min
Advanced outputs with Andrea
Climate report and processed data
05
min
Questions and next steps
Connect the map to Module 3

## Slide 3
A project question becomes five choices
The choices come before the first map click
CAVA MODULE 2
03
How will extreme heat change in our project area over the next 30 years?
01
Area
Which geography or project boundary?
02
Indicator
What represents extreme heat?
03
Reference
What historical period is the comparison?
04
Scenario
Which future pathway?
05
Horizon
Which future period matters for the decision?
Teaching example: the threshold and location should reflect the actual project question.

## Slide 4
The Platform at a glance
Three places to look before interpreting a map
CAVA MODULE 2
04
Public map view captured 22 September 2026
LEFT
Browse climate and agriculture layers
CENTRE
See the spatial pattern
RIGHT
Check the legend and units
Notes: Current public CAVA Platform overview captured for the updated interface. Source: https://cavaplatform.fao.org/map

## Slide 5
The indicator and historical reference
Live demonstration: select the heat layer and read its settings
CAVA MODULE 2
05
Public map: Hot Tmax days (≥35°C), observations, annual view
LAYER
Climate › Heat & Cold
INDICATOR
Hot Tmax days ≥35°C
REFERENCE
Observations, 1991–2020
Notes: Current public CAVA Platform state: Climate, Heat & Cold, Hot Tmax days above 35 degrees Celsius, historical observations. Source: https://cavaplatform.fao.org/map

## Slide 6
A future climate view
Keep the indicator fixed while changing scenario and time horizon
CAVA MODULE 2
06
Public map: RCP 8.5, 2070–2099, annual value view
SCENARIO
Choose a future pathway
PERIOD
Select the project-relevant horizon
READING
The value map shows future conditions
Notes: Current public CAVA Platform state: Hot Tmax days above 35 degrees Celsius, future value under RCP 8.5 for 2070–2099. Source: https://cavaplatform.fao.org/map

## Slide 7
Change needs a reference period
The map changes meaning when “Value” becomes “Change”
CAVA MODULE 2
07
Public map: RCP 8.5, 2070–2099 change from 1986–2005
COMPARE
Switch from Value to Change
BASELINE
Read the reference period
UNITS
Check whether the legend shows days or degrees
Notes: Current public CAVA Platform state: change in Hot Tmax days above 35 degrees Celsius relative to the 1986–2005 baseline. Source: https://cavaplatform.fao.org/map

## Slide 8
Reading a climate signal
A map is the beginning of interpretation
CAVA MODULE 2
08
01
Magnitude
How large is the difference, in the legend’s units?
02
Pattern
Is the signal widespread or localized?
03
Comparison
Which baseline, scenario and future period are selected?
04
Confidence
What do other models or available analyses show?
Interpret the output alongside the project’s exposure, vulnerability and decision context.

## Slide 9
YOUR TURN
Try the same workflow
for your area
01
Choose a geography and relevant indicator
02
Select a future scenario and period
03
Compare Value and Change, then read the units
Be ready to describe one pattern and one uncertainty.

## Slide 10
Advanced outputs
Andrea’s live demonstration: outputs that travel beyond the map
CAVA MODULE 2
10
PDF
Climate report
Key climatologies and analyses for discussion and project documentation
XLSX
Processed climate data
Structured inputs for further analysis and downstream impact modelling
The live demonstration will show the available request and download steps.

## Slide 11
BEFORE YOU LEAVE
Can you explain the map
without the map?
01
The indicator and its units
02
The scenario, periods and baseline
03
The signal, and what remains uncertain
Next: Module 3 · Climate data workflows with cavapy and CAVAanalytics